## Slide 1
The Eastern Goldfields High Resolution Seismic Survey:
preliminary interpretation and tectonic implications
Ivan Zibra
Klaus Gessner, Jyotindra Sapkota, Matt De Paoli, Roberto Weinberg, Mike Dentith, Ruth Murdie, Renfei Tian, Huaiyu Yuan

## Slide 2
Transpressional Ballard shear zone
(≥200 km along strike. Zibra et al., 2020 -Tectonics)
Kalgoorlie Terrane shaped by:
Active in c. 2680-65 Ma
2 Structural Elements
HT Gneiss
Mylonite
Notes: BSZ responsible for bulk of structural architecture in the kal terrane

## Slide 3
(1) Granitic gneiss: HT fabric
Most of granitic domain
Melt-present deformation
high strain
low strain
1–2 km thick SL tectonite
Grain size reduction
(2) Mylonitic domain
Notes: This is a pervasive, HT fabric homogeneously developed across 10-30 km-wide shear zones. Typical high-strain and low-strain microstructure. Red arrow points to synmagmatic microfracture

## Slide 4
Zibra et al.
(2020 - Tectonics)
Strain partitioning
Crustal extrusion
Large-scale
Local normal SZ
In bulk shortening
Notes: The extrusion model, in a few words, which derives from kinematic partitioning between cold greenstone and hot sheets of crystallizing granite

## Slide 5
Kalgoorlie Terrane:
First-order (large-scale) tectonic scheme
Two regional transpressional events during bulk E-W shortening
Sedimentary response to crustal thickening
Crosscutting, undeformed granites
Two
cross sections
Two regional-scale
tectonic events
Notes: Waroonga is similar story but different geometry (W dipping) but still reflecting E-W shortening. So, at the temporal resolution that we have now, the area seems to have recorded shortening for c. 20 Myr. Reality is likely that there were pulses during injection of granite sheets, alternating with periods of tectonic quiescence

## Slide 6
Zuleika sz: Southern continuation (reactivation) of Ballard sz
V
V
V
V
V
V
V
V
V
V
(ii) Structural basin ( shallow crustal level)
Swager et al. (1990)
Kalgoorlie area:
Notes: Important for seismic interp: Kalgoorlie area is structural basin (convergence of north- and south-plunging folds), higher structural level thank Ballard sz in the north. The BSZ is therefore visible in the lower portions of our new seismic profiles.
Zuleika is a D2 structure (see time sketch at slide #13), likely reactivating the lower portion of the Ballard SZ, at higher structural levels (so more localized and exploiting lithological boundaries in greenstones; as opposed to hotter, broader & pervasive fabric along the Ballard)

## Slide 7
Kalgoorlie area - Structural style:
Shear zone nucleation along steep fold limbs
Dias et al. 2008
Broad zones of contraction (strong layers: mafic-U.mafic)
Narrow zones of simple shear (weak layers: BFG)
FACTORS PROMOTING SHEAR LOCALIZATION:
Higher structural level than Ballard sz area
(up to 10 km shallower?)
No synmagmatic shearing
Notes: The Ballard+ waroonga SZ evolution teaches us that strain partitioning must have played a key role in the Kalgoorlie area. But it is very difficult to see, as zones of simple shear may have been knife-sharp and might be exposed in some pits only

## Slide 8
Younger reactivation
Low-grade
Thrust-sinistral
Network of ~10m-thick SZs exploiting infra-greenstones
lithological boundaries
- No overprint in Ballard gneisses
Weinberg et al., 2002
Notes: Fundamental point for backbone concept: the ballard fabric gets reused later at lower-T, note that Zuleika is highly mineralized. So far the 2 structures are considered coeval, but clearly they are not (see time constraints at left)

## Slide 9
Timeframe:
Early 2019:
Acquisition, processing (Velseis)
July–August 2019:
Preliminary Interpretation and report compilation
(Velseis with GSWA support)
September 2019: data released to public
2020–2021:
Structural-geophysical investigations (GSWA)
Hi-Res Reflection Survey
7 lines = 305 km
Depth: 5 s Two-way time (~12 km, for v=5 km/s)
Notes: Just a few words, also as a ‘disclaimer’ as we do not have our interpr for now

## Slide 10
Drummond et al. (2000)
Kalgoorlie area – crustal architecture
East-dipping fabric
Local west-dipping,
upper crustal structures
Notes: Broadly speaking, we have a series of contractional pop ups, with main east dipping sz (Ida, Ballard-Zuleika) and a series of shallower, west-dipping ones, which in map view form a series of anastomosing splays

## Slide 11
2D Seismic survey - Synthetic view
Main structures can be traced across several lines  rough 3D geometry
Notes: Just a very preliminary attempt to correlate structures across profiles. Result is encouraging, as we can follow main shear zones quite well

## Slide 12
Main lithotectonic elements:
Kalgoorlie Group: strong reflectors
Upper (felsic) succession: transparent
Granites & Gneisses: reflective to transparent
Proterozoic dykes: reflective to transparent
Zones of alteration (?)
2019 seismic survey: key features
0.5 s
(~1250 m)
Notes: Arrows indicate:
1- Kalgoorlie group
2- metasediments/felsic volc
3-granite
4- granite gneiss
(Prot dykes not visible here)
5- alteration (?) zones
shear zones mainly identified by spotting offsets in the strong markers of the Kalgoorlie group

## Slide 13
Open, parallel folds
Overall listric structures
2019 seismic survey: key features
0.5 s
(~1250 m)
Notes: Open, parallel and kink folds, as expected at upper crustal levels.
Shear zones with overall listric geometry, replicating what’s visible in crustal-scale profiles

## Slide 14
High-resolution
data
(W end of line 4)
0.5 s
(~1250 m)
Notes: Overall, when you zoom in there is a lot of detail in the data, so there is a lot of room for anyone to play and provide your own interpr.

## Slide 15
EGF Geophysical Project
Led by Prof Mike Dentith, UWA
EIS-funded by GSWA
Passive seismic survey along EGF01 deep reflection line
    Kanowna Belle, Paddington
60 station long period MT survey (as far west as Southern Cross)
Broad band MT survey planned
Passive Seismic MT (Blue = new data)
EGF1
Kalgoorlie
Norseman
Coolgardie
EGF01
KB
Pa

## Slide 16
Lo
w
er
basalt
F
elsic
gneiss
K
omatiite
Ear
ly
g
r
anite
Upper
basalt
Late
g
r
anite
Bullab
ulling
Shear
K
unanalling
Shear
Ida
F
ault
Zuleika
Shear
Em
u
F
ault
Arcoona
Gr
anite
Scotia-Kano
wna
Anticline
Mt
Pleasant
Anticline
K
urr
a
w
ang
Syncline
Dunnsville
Anticline
KALGOORLIE
TERRANE
KURNALPI
TERRANE
0
5
10
15
D
e
p
t
h
(
k
m
)
Bar
doc
Def
ormation
Zone
Mount
Mong
er
F
ault
Greenstone
sequence
(in
Bardoc
Shear
Zone)
F
elsic
v
olcanic
roc
ks
Undivided
basalt
F
elsic
v
olcanic
unit
Basal
f
elsic
schist
W
E
Kalgoorlie
EGF1
0
Basal
detachment
?
10
km
CMP
4000
6000
5000
7000
9000
8000
20 km
15
10
5
0
45
30
15
0
Two-way Time (s)
Approx’ Depth (km)
Moho
Less Coherent
Reflectivity
Imbricate Thrusting
Imbricate Thrusting
Greenstones
Source: Local explosion/
vibration
Moho
Reflection Data
EGF01 deep reflection profile
‘Detached’ greenstone sequence
Complex lower crust
Reduced reflectivity in the Kalgoorlie terrane

## Slide 17
CMP
4000
6000
5000
7000
9000
8000
20 km
15
10
5
0
45
30
15
0
Two-way Time (s)
Approx’ Depth (km)
Moho
Imbricate
Thrusting
Imbricate Thrusting
10
100
1000
Resistivity
(W.m)
Greenstones
Long period MT data
Graham Heinson, Univ’ of Adelaide
Short term deployment of 18 stations using experimental equipment
Kalgoorlie terrane anomalously conductive
Especially conductive at base of greenstones near the Bardoc SZ
Lateral changes in upper mantle conductivity
Moho
Magnetotellurics
Natural EM
energy
Less Coherent
Reflectivity

## Slide 18
CMP
4000
6000
5000
7000
9000
8000
20 km
15
10
5
0
45
30
15
0
Two-way Time (s)
Approx’ Depth (km)
Moho
Imbricate Thrusting
Imbricate Thrusting
1.76
1.68
1.72
Vp/Vs
Greenstones
H-k analysis (crustal thickness and Vp/Vs)
Moho 35-40 km
Increase in Vp/Vs in Eastern Goldfields Superterrane (~1.72 to ~1.75)
Moho
Teleseismic Data
From Distant
Earthquakes
Greenstones at surface
Less Coherent
Reflectivity

## Slide 19
CMP
4000
6000
5000
7000
9000
8000
20 km
15
10
5
0
45
30
15
0
Two-way Time (s)
Approx’ Depth (km)
Moho
Imbricate Thrusting
Imbricate Thrusting
1.76
1.68
1.72
Vp/Vs
Greenstones
Common conversion point stacked section
Stack receiver functions according to zone where encounter crust and are converted
Excellent correlation with reflection section
Strong Moho response
Positive velocity contrast below base of the greenstones
Less Coherent
Reflectivity
Moho
Teleseismic Data
From Distant
Earthquakes

## Slide 20
CMP
4000
6000
5000
7000
9000
8000
20 km
15
10
5
0
45
30
15
0
Two-way Time (s)
Approx’ Depth (km)
Moho
Imbricate Thrusting
Imbricate Thrusting
1.68
Greenstones
Ambient noise tomography
Crustal thickness consistent with other estimates
Excellent correlation with reflection section
High (~4.0 km/s) over low (~3 km/s) over high (~4.3 km/s) Vs anomalies under greenstones in Kalgoorlie Terrane
Fault controlled?
Moho
Ambient Noise Data
From Distant
Micro Seismic
Events
Note reverse spectrum display
Vs
Less Coherent
Reflectivity

## Slide 21
EGF Geophysical Project
Summary – central Kalgoorlie Terrane
Zone of reduced reflectivity (reflection)
Increased conductivity (MT
Layered structure at base of greenstones (teleseismic)
Increase in Vp/Vs (teleseismic)
High-low-high structure beneath greenstones in shear-wave velocity (ambient noise)
Structurally controlled
Vp/Vs
Reflection Coherence
Conductivity
Velocity Contrast
Vs
Reflection Coherence
Kalg’ Terrane at Surface

## Slide 22
SUMMARY: work in progress, watch this space …
Mapping and geochronology established a tectonic model with the ~2680–50 Ma Ballard shear zone as a ‘Yilgarn Backbone’ accommodating E–W shortening, crustal thickening, and a coeval sedimentary response.
2019 Kalgoorlie seismic survey – preliminary assessment: key features consistent with local and Yilgarn-wide data
Passive seismic and MT project produces further constraints to the EGF crustal architecture, tectonic evolution and mineralization.
Notes: Emphasizing that the idea is to use observations from well exposed regional structures (Ballard, Waroonga, but also the ones in the west) to picture the broad tectonic style.
A brief conclusion on the new data is that, although we are in very early days with interpr, the new data seem to fit well with the existing ones.
 You can also mention what we discussed in the meeting, future outlooks from gswa side (integrating geochem, 3D modelling, etc)